## Slide 1: Computers Are Your Future Twelfth Edition
Chapter 2: Inside the System Unit
CPIT 220
Dr. Sabeen Tahir

## Slide 2: Inside the Computer System

## Slide 3: Objectives
Understand how computers represent data.
Understand the measurements used to describe data transfer rates and data storage capacity.
List the components found inside the system unit and explain their use.

## Slide 4: Objectives
List the components found on the computer’s motherboard and explain their role in the computer system.
Discuss (in general terms) how a CPU processes data.
Explain the factors that determine a microprocessor’s performance.

## Slide 5: Objectives
List the various types of memory found in a computer system and explain the purpose of each.
Describe the various physical connectors on the exterior of the system unit and explain their use.

## Slide 6: How Computers Represent Data
Binary numbers
  Only 0s and 1s
Bit
  Smallest piece of data a computer can work with
  Either “on” or “off,” a 0 or a 1
  Eight bits—byte—a single unit of storage

## Slide 7: How Computers Represent Data
Modem’s data transfer rate is in bits per second
  Example—gigabits per second (Gbps)
Data storage is in bytes
  Kilobyte (KB)—one thousand bytes
  Megabyte (MB)—one million bytes
  Gigabytes (GB)—one billion bytes
  Terabyte (TB)—one trillion bytes

## Slide 8: How Computers Represent Data
Computers convert binary numbers into hexadecimal (hex) numbers
  Which use the numbers 0 through 9, followed by letters A through F

## Slide 9: How Computers Represent Data
Floating point notation
  Has no fixed number of digits before or after a decimal point
  Enables a computer to work quickly with very large or small numbers
  Requires special processing circuitry

## Slide 10: How Computers Represent Data
Characters
  Letters, numbers, and symbols—converted into numbers the computer understands
Character code
  Performs the conversion
    American Standard Code for Information Interchange (ASCII)
    Extended Binary Coded Decimal Interchange Code (EBCDIC)
    Unicode

## Slide 11: Introducing the System Unit
System unit
  Case that contains the major hardware components of a computer
  Come in different styles
  Footprints
    Amount of space that the unit uses

## Slide 12: Introducing the System Unit
System unit (con’t.)
  Some have embedded biometric authentication devices such as fingerprint readers, retina scanners, and face recognition systems to prevent unauthorized access.
  Form factor—specifies how the internal components are located within the system unit.

## Slide 13: Inside the System Unit

## Slide 14: Inside the System Unit
Motherboard
CPU
Power supply
Cooling fan
Internal speaker
Drive bays
Expansion slots
System unit main components

## Slide 15: Inside the System Unit

## Slide 16: Inside the System Unit

## Slide 17: What’s on the Motherboard?

## Slide 18: What’s on the Motherboard?
Motherboard
  Printed circuit board that contains the electrical circuitry for the computer
  The majority of parts found on the motherboard are integrated circuits.
    Includes millions of transistors and carries electrical current
      A switch that is able to control the electrical signal flow to the circuit

## Slide 19: What’s on the Motherboard?
Central processing unit (CPU)
  Integrated circuit chip that processes electronic signals
  Also known as a microprocessor or processor

## Slide 20: What’s on the Motherboard?
CPU (con’t.)
  Is usually covered by a heat sink
    A heat-dissipating component that drains heat from the chip
  Instruction—An operation performed by the CPU and assigned a specific number
  Instruction set—The list of CPU instructions for the operations

## Slide 21: What’s on the Motherboard?
CPU (con’t.)
  Control unit—one of the two main parts
    Retrieves instructions from memory
    Interprets and performs those instructions
    Manages the machine cycle or processing cycle, the four-part process performed by the CPU
  Arithmetic logic unit (ALU)—one of the two main parts
    Performs arithmetic and logical operations
      Involve adding, subtracting, multiplying, dividing
      Logical operations involve comparisons between two or more data items.

## Slide 22: What’s on the Motherboard?
Machine cycle
  Instruction cycle
    Fetch: Retrieves program instructions
    Decode: Determines what the program is telling the computer to do
  Execution cycle:
    Execute: Performs the requested action
    Store: Stores the results to an internal register
Registers—store data when it must be temporarily stored in the CPU

## Slide 23: What’s on the Motherboard?

## Slide 24: What’s on the Motherboard?
Factors that affect the performance of a CPU include:
  Number of existing transistors
  Data bus width and word size
  Clock speed
  Operations per microprocessor cycle
  Use of parallel processing
  Type of chip

## Slide 25: What’s on the Motherboard?
Data bus
  Group of parallel wires that connect the CPU’s internal components
  Width measured in bits
  Maximum number of bits the CPU can process at once is called the word size
    Determines which operating systems and software a CPU can run

## Slide 26: What’s on the Motherboard?
  System clock
    Electronic circuit that produces rapid pulses and coordinates the computer’s internal activities.
    Clock speed—measurement of the electrical pulses generated by the system clock, usually measured in gigahertz (GHz)

## Slide 27: What’s on the Motherboard?
  System clock (con’t.)
    Superscalar architecture—enables the CPU to perform more than one instruction for each clock cycle
    Pipelining—enables the CPU to process more than one instruction at a time improving performance

## Slide 28: What’s on the Motherboard?

## Slide 29: What’s on the Motherboard?

## Slide 30: What’s on the Motherboard?
Parallel processing
  Method where more than one processor performs at the same time—faster processing

## Slide 31: What’s on the Motherboard?
Multi-core processing
  Access time reduced
  Processing time improved
  Each core handles incoming streams of data or instructions at the same time
  Two basic types:
    Dual core
    Quad core

## Slide 32: What’s on the Motherboard?
Chipset
  Set of chips that supply the switching circuitry the CPU requires to move data throughout the computer
  The CPU and the input/output (I/O) bus linked through the chipset
    Provides a means to communicate with input and output devices

## Slide 33: What’s on the Motherboard?
Memory
  Chips on the motherboard or within the CPU that retain instructions and data
Random access memory (RAM)
  Temporarily stores data and instructions for the CPU
  Volatile—contents erased after computer is shut off
  Allows CPU to access or store data and instructions quickly through RAM’s memory address feature
    Identifies and locates stored data

## Slide 34: What’s on the Motherboard?

## Slide 35: What’s on the Motherboard?
RAM (con’t.)
  Comes in the form of memory modules or memory cards
  Memory modules (memory cards)—small circuit boards that hold several RAM chips and fits into special slots on the motherboard
  Types of RAM:
    Dual inline memory modules (DIMM)—most common today
      168-pin connector
      64-bit transfer rate
    Single inline memory modules (SIMM)—older technology
      72-pin connector
      32-bit transfer rate

## Slide 36: What’s on the Motherboard?
Memory footprint
  Amount of RAM the operating system uses while it operates
Virtual memory
  Section of the hard drive set aside to use when RAM gets full

## Slide 37: What’s on the Motherboard?
Cache memory
  Small unit of ultrafast memory built into or near the processor
  Used to store frequently or recently access program instructions or data
  Faster than RAM
  More expensive than RAM
  Three levels of cache on a system:
    Level 1 (L1) cache (primary cache)
    Level 2 (L2) cache (secondary cache)
    Level 3 (L3) cache
      Found on some newer microprocessors
      Primarily used in servers and workstations

## Slide 38: What’s on the Motherboard?

## Slide 39: What’s on the Motherboard?
Read-only memory (ROM)
  Contains prerecorded instructions to start the computer
  Nonvolatile—contents stored when CPU power off
    Basic input/output system (BIOS)
      First code run when the system is powered on
    Bootstrap loader
      Program—locates and loads the operating system into RAM
    Complementary metal-oxide semiconductor (CMOS)
      Starts the power-on self-test and verifies other system components are operating correctly
    Power-on self-test (POST)
      Checks circuitry and RAM, marking defective locations

## Slide 40: What’s on the Motherboard?
ROM (con’t.)
  Programmable ROM (PROM)
    Electrically-PROM (EPROM)
  Electrically erasable PROM (EEPROM)
  Flash EPROM

## Slide 41: What’s on the Outside of the Box?
Front panel
  Power switch
    Used to turn the computer on
  Drive activity light
    Advises the user that the hard drive is retrieving data
  Power-on light
    Shows whether the power is on

## Slide 42: What’s on the Outside of the Box?
  Outside a system unit
    Connector—physical receptacle used to plug a peripheral device into the computer
      Example: telephone jack
    Port—electronically defined pathway used to send data into and retrieve data from the computer
      Example: USB port

## Slide 43: What’s on the Outside of the Box?

## Slide 44: What’s on the Outside of the Box?
Connectors on a notebook may vary
Notes: This is Figure 2.29.

## Slide 45: What’s on the Outside of the Box?
USB (universal serial bus) ports
  Connects up to 127 peripheral devices
  USB 2.0 (high-speed USB)—fully compatible with USB 1.1 products, cables, and connectors
  Designed to replace older parallel and serial ports
  Connects a variety of devices to the computer, including:
    Keyboards
    Mice
    Printers
    Digital cameras

## Slide 46: What’s on the Outside of the Box?
USB 2.0
  Uses an external bus
  Supports data transfer rates of 480 Mbps between the computer and the peripheral device
  Supports hot swapping—ability to connect and disconnect devices without shutting down the computer
  Plug-and-play (PnP)—allows computers to automatically detect the device when you plug it in
USB hub
  Device that plugs into existing USB port
  Contains four or more additional ports
Notes: This is Figure 2.20.

## Slide 47: What’s on the Outside of the Box?
FireWire (1395 ports)
  Created by Apple in 1995
  IEEE 1394 Higher Performance Serial Bus, also known as Sony i.Link
  Offers high-speed connections for dozens of peripheral devices (up to 63)
  Enables hot swapping and PnP
  Data transfer rates of FireWire
    FireWire 400—400 Mbps
    FireWire 800—800 Mbps
    FireWire S3200—next generation (expected to transfer data at 3.2 Gbps)
Notes: This is Figure 2.20.

## Slide 48: What’s on the Outside of the Box?
Video connectors
  VGA (video graphics array)
    15-pin male connector—works with standard monitor cables
    Transmits analog video signals
    Used for legacy technology cathode ray (CRT) monitors
  DVI (Digital visual Interface) port—lets LCD monitors use digital signals
  Onboard video—video circuitry built into the motherboard where the video connector is on the back of the system unit case
Notes: This is Figure 2.20.

## Slide 49: What’s on the Outside of the Box?
Additional connectors
  Telephone
  Network
  PC card slot
    PC card
    ExpressCard
  Sound card
  Game card
  TV/sound capture board

## Slide 50: What’s on the Outside of the Box?
Legacy technology
  Older technology that is being phased out
    Examples:
        Serial ports
        Parallel ports
        PS/2 ports
        SCSI (small computer system interface) ports

## Slide 51: Summary
Understand how computers represent data.
Understand the measurements used to describe data transfer rates and data storage capacity.
List the components found inside the system unit and explain their use.

## Slide 52: Summary
List the components found on the computer’s motherboard and explain their role in the computer system.
Discuss (in general terms) how a CPU processes data.
Explain the factors that determine a microprocessor’s performance.

## Slide 53: Summary
List the various types of memory found in a computer system and explain the purpose of each.
Describe the various physical connectors on the exterior of the system unit and explain their use.

## Slide 54
All rights reserved. No part of this publication may be reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise, without the prior written permission of the publisher. Printed in the United States of America.
Copyright © 2012 Pearson Education, Inc.
Publishing as Prentice Hall