## Slide 1: Computers Are Your Future Twelfth Edition
Chapter 7: Networks: Communicating
and Sharing Resources

## Slide 2: Networks: Communicating and Sharing Resources

## Slide 3: Objectives
Understand basic networking concepts.
Distinguish between a WAN, LAN, MAN, CAN, HAN, and PAN.
Discuss the advantages and disadvantages of networks.
Distinguish between peer-to-peer, client/server, and virtual private local area networks (LANs).

## Slide 4: Objectives
Define topology and understand how the three LAN topologies differ.
Explain the importance of network protocols.
Name the most widely used LAN protocol and their versions.
Identify the special components of a wide area network (WAN) that differentiate it from a LAN.

## Slide 5: Objectives
Contrast circuit-switching and packet-switching networks and explain their respective strengths and weaknesses.
Identify the options, components, configuration, and maintenance of a home area network (HAN).

## Slide 6: Network Fundamentals
Networks
  Links multiple computer systems and enables them to share data and resources
  Types of computer networks:
    Local area network (LAN)
    Wide area network (WAN)
    Metropolitan area network (MAN)
    Campus area network (CAN)
    Personal area network (PAN

## Slide 7: Network Fundamentals
Notes: T

## Slide 8: Network Fundamentals
LAN
  Uses cables, radio waves, or infrared signals
  Links computers in a limited geographic area
WAN
  Uses long-distance transmission media
  Links computer systems a few miles or thousands of miles
  Internet is the largest WAN
MAN
  Designed for a city
  Larger than a LAN, smaller than a WAN

## Slide 9: Network Fundamentals
CAN
  Several LANs located in various locations on a college or business campus
  Smaller than a WAN
  Use devices such as switches, hubs, and routers
PAN
  Network of an individual’s own personal devices
  Usually within a range of 32 feet
  Usually use wireless technology

## Slide 10: Network Fundamentals
Communication devices
  Convert data into signals to travel over a medium
    Computers
    Modems
    Routers
    Switches
    Hubs
    Wireless access points
    Network interface cards (NICs)

## Slide 11: Network Fundamentals
Node
  Any device connected to a network
Logical address
  Unique name assigned to each node on the network
Physical address
  Unique numeric that identifies each node on the network built into the hardware
Network interface card (NIC)
  Expansion board or adapter that provides a connection between the computer and the network
  Notebook computers have wireless NICs

## Slide 12: Network Fundamentals

## Slide 13: Network Fundamentals
USB wireless network adapter
  Plugs into a USB port
  Usually provides an intuitive graphical user interface (GUI) for easy configuration
USB dongle
  Device inserted into a USB port that adds additional features to the base system
  Examples: enabling network connectivity and increasing RAM
Wireless PC card adapter
  About the size of a credit card
  Inserted into a slot on the side of most notebooks and netbooks
  Has built-in WiFi antenna that provides wireless capability
  LED lights that indicate whether the computer is connected

## Slide 14: Network Fundamentals
Hub
  Joins multiple computers together in a single network
  Does not manage traffic between the connections
Switches
  Filter and forward data between nodes
  Are similar to routers but work within a single network
Routers
  Connect two or more networks
  Inspect the source and target of a data package
  Determine the best route to transmit data

## Slide 15: Network Fundamentals
Wireless access point (WAP)
  Receives and transmits radio signals
  Joins wireless nodes to a wired network

## Slide 16: Network Fundamentals
Server
  Computer or device with software that manages network resources, such as files, e-mails, printers, databases
File server
  Most common type of server
  High-speed computer that provides program and data files to network users
  Contains the network operating system (NOS)
    File directories for file and resource location on the LAN
    Automated distribution of software updates to desktop computers on the WAN
    Internet services support
    Protection of services and data
    Access to connected hardware by authorized users

## Slide 17: Network Fundamentals
Network administrator
  Also called network engineer
  Installs, maintains, supports computer networks
  Interact with users
  Handle security
  Troubleshoot problems

## Slide 18: Advantages and Disadvantages of Networking
Networking
  Advantages
    Reduced hardware costs
    Application sharing
    Sharing information resources
    Data management centralization
    Connecting people
  Disadvantages
    Loss of autonomy
    Lack of privacy
    Security threats
    Loss of productivity

## Slide 19: Local Area Networks
Peer-to-peer (P2P) networks
  Share files without a file server
  Easy to set up
  Best used for home or small offices with no more than 10 computers
  Do not require a network operating system
  Can be slow if there are too many users
  Security not strong

## Slide 20: Local Area Networks
Peer-to-peer (P2P) networks

## Slide 21: Local Area Networks
Wireless LAN
  Connects users through radio waves instead of wires
  Use includes networks in:
    Homes
    Hospitals
    Colleges
  Secured with a radio transmission technique that spreads signals over a seemingly random series of frequencies.
  Effective inside range of between 125 and 300 feet

## Slide 22: Local Area Networks

## Slide 23: Local Area Networks
Client/server networks
  Made up of one or more file servers and clients (any type of computer)
  Client software enables requests to be sent to the server
  Wired or wireless connections
  Do not slow down with heavy use

## Slide 24: Local Area Networks

## Slide 25: Local Area Networks
Intranet
  Password-protected network controlled by the company
  Accessed only by employees
Virtual private network
  Operates over the Internet
  Accessible by authorized users for quick access to corporate information
  Uses secure, encrypted connections and special software

## Slide 26: Local Area Networks
LAN topologies
  Network topology
    Physical design of a LAN
  Topology resolves contention—conflict that occurs when two or more computers on the network attempt to transmit at the same time
  Contention sometimes results in collisions—corruption of network data caused when two computers transmit at the same time

## Slide 27: Local Area Networks
LAN topologies
  Bus topology
    Practical for home or small office
    One node transmits at a time
    Terminators signify the end of the circuit
    Uses contention management—technique that specifies what happens when a collision occurs
  Star topology
    For office buildings, computer labs, and WANs
    Easy to add users
  Ring topology
    For a division of a company or one floor
    Not in common use today
    Node can transmit only when it has the token—special unit of data that travels around the ring

## Slide 28: Local Area Networks

## Slide 29: Local Area Networks

## Slide 30: Local Area Networks

## Slide 31: Local Area Networks
LAN protocols
  Protocols—standards used by networks to permit communication between network-connected devices
  Modulation protocols—ensure that the modem can communicate with another modem, even if by a different manufacturer
  Protocol suite—contains the protocols of the network and specifies its network architecture, or how the network works

## Slide 32: Local Area Networks
LAN protocols (con’t.)
  Network layers—divide network architecture for separate treatment
    Each network layer can operate and be governed by its own protocols.
    Protocol stack—vertical arrangement of network layers

## Slide 33: Local Area Networks
LAN technologies
  Ethernet—most-used LAN protocol
    Ethernet star networks
      Most popular versions—use twisted-pair wiring and switches
    Sends data in a fixed-size unit called a packet
  WiFi
    Uses radio waves to provide a wireless LAN standard at Ethernet speeds
    Needs a central access point—could be a wireless router
    Hot spots—public wireless access locations

## Slide 34: Wide Area Networks
Point of presence (POP)
  WAN connection point used to obtain access to the WAN
  Wired or wireless
Backbones
  High-capacity WAN transmission lines
  gigaPoP (gigabits per second point of presence)—transfers data exceeding 1 Gbps (1 billion bits per second)

## Slide 35: Wide Area Networks
WAN protocols
  Internet protocols
    Transmission Control Protocol/Internet Protocol (TCP/IP)
      Protocols that define how the Internet works
    Transmission Control Protocol (TCP)
      Defines how Internet-connected computers can exchange, control, and confirm messages
    Internet Protocol (IP)
      Provides a distinct identification to any computer connected to the Internet: the IP address or Internet address

## Slide 36: Wide Area Networks
WAN protocols (con’t.)
  Circuit switching
    Used by the public switched telephone network to send data over a physical end-to-end circuit
    Provides a direct connection between devices
  Packet switching
    Used for computer communication
    Divides and sends outgoing messages as packets, which are reassembled on receipt
    More efficient and less expensive than circuit switching
  Latency—delay introduced when a given packet is examined by many routers
  Congestion—occurs when the network is overloaded, causing some packets to be further delayed

## Slide 37: Wide Area Networks

## Slide 38: Wide Area Networks

## Slide 39: Wide Area Networks

## Slide 40: Wide Area Networks

## Slide 41: Wide Area Networks
WAN applications
  E-mail, conferencing, document exchange, remote database access
  LAN to LAN connections connect two or more geographically separate locations
  Transaction acquisition—the instant relay of transaction information from a point-of-purchase sale.

## Slide 42: Home Networks
Home Area Networks (HANs)
  Wired home networks
  Wireless home networks
  Hybrid networks
    Combination of wired and wireless technology

## Slide 43: Home Networks
A Wired Home Network

## Slide 44: Home Networks
A Wireless Home Network

## Slide 45: Home Networks
Setting up a home network
  Planning
    Select technology
    Purchase equipment and firewall software
  Configuring a wired network
    Connect each computer to the router
    Plug printer, scanner, etc., into a computer

## Slide 46: Home Networks
Setting up a home network (con’t.)
  Configuring a wireless network
    Connect each node to wireless router with a wireless adapter
    Connect DSL or cable modem to wireless router
  Maintenance and support
    Minimal maintenance required
    Unplug power source from router and other peripherals and restart computer to correct problems

## Slide 47: Home Networks
Future of home networking
  Convergence will allow you to use home networks to
    Control household appliances
    Protect homes with security systems
    Manage home network events through central control units in new homes
    Utilize wireless systems
    Control entertainment, temperature regulation, and lighting

## Slide 48: Summary
Understand basic networking concepts.
Distinguish between a WAN, LAN, MAN, CAN, HAN, and PAN.
Discuss the advantages and disadvantages of networks.
Distinguish between peer-to-peer, client/server, and virtual private local area networks (LANs).

## Slide 49: Summary
Define topology and understand how the three LAN topologies differ.
Explain the importance of network protocols.
Name the most widely used LAN protocol and their versions.
Identify the special components of a wide area network (WAN) that differentiate it from a LAN.

## Slide 50: Summary
Contrast circuit-switching and packet-switching networks and explain their respective strengths and weaknesses.
Identify the options, components, configuration, and maintenance of a home area network (HAN).

## Slide 51
All rights reserved. No part of this publication may be reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise, without the prior written permission of the publisher. Printed in the United States of America.
Copyright © 2012 Pearson Education, Inc.
Publishing as Prentice Hall