## Slide 1: Computers Are Your Future Twelfth Edition
Chapter 8: Wired and Wireless Communication

## Slide 2: Wired and Wireless Communication

## Slide 3: Objectives
Differentiate between bandwidth and throughput, and discuss the bandwidth needs of typical users.
Discuss how modems transform digital computer signals into analog signals and analog into digital.
List various physical and wireless transmission media and explain several transmission methods.

## Slide 4: Objectives
Explain the limitations of the public switched telephone network (PSTN) for sending and receiving computer data.
Describe digital telephony and multiplexing, including their impact on line usage.
Discuss last-mile technologies that connect users with their communication providers.

## Slide 5: Objectives
Provide examples of how digitization and convergence are blurring the boundaries that distinguish popular communications devices, including phones and computers.
Discuss various wired and wireless applications.

## Slide 6: Moving Data: Bandwidth and Modems
Communications
  Process of sending and receiving messages electronically between two points
  Sending device—initiates the transmission
  Receiving device—accepts the transmission and responds
Communications channel
  Path to send and receive messages

## Slide 7: Moving Data: Bandwidth and Modems
Analog signals
  Continuous waves
Digital signals
  Discontinuous, discrete pulses
Converters
  Translate signals:
    Analog-to-digital converter (ADC)
    Digital-to-analog converter (DAC)

## Slide 8: Moving Data: Bandwidth and Modems
Digital signal sampling

## Slide 9: Moving Data: Bandwidth and Modems
Bandwidth
  The maximum amount of data transmitted through a communication channel at one time
Throughput
  The actual amount of data transmitted

## Slide 10: Moving Data: Bandwidth and Modems
Broadband
  Any transmission medium that carries several channels transporting data at high speeds
Streaming
  The ability to hear or see content while it is being downloaded from a Web site

## Slide 11: Moving Data: Bandwidth and Modems
Modem
  A communication device used to send and receive data
  The term modem comes from modulate and demodulate.
    The sender uses modulation to transmit digital signals.
    The receiver uses demodulation to return signals to digital form.

## Slide 12: Moving Data: Bandwidth and Modems

## Slide 13: Moving Data: Bandwidth and Modems
Types of modems
  Analog
  Digital subscriber line (DSL)
  Cable
  Integrated Services Digital Network (ISDN)
Data transfer rate
  Rate at which two modems exchange data
  Measured in bits per second (bps)
Baud
  Number of signaling elements per second

## Slide 14: Wired Transmission Media
  Wiring closet
    Houses wiring that supports most types of data transfer needed

## Slide 15: Wired Transmission Media
  Twisted-pair wire
    Copper wire used for telephone and data communication
    Two pairs of interweaved wires twisted together
    Inexpensive, but bandwidth too low for video, voice, and data at the same time

## Slide 16: Wired Transmission Media
Key variations of twisted-wire pair
    Category 5 (Cat-5)
    Category 5 enhanced (Cat-5e)
    Category 6 (Cat-6)

## Slide 17: Wired Transmission Media
Coaxial cable
  Consists of copper wire surrounded by insulation and braided wire
    Broadband communication
    Cable TV
    10 Mbps transfer rate

## Slide 18: Wired Transmission Media
Fiber-optic cable
  Consists of thin strands of glass or plastic that carry data through pulses of light
    Broadband communication
    10 Gbps transfer rate

## Slide 19: Wireless Transmission Media
  Infrared
    Wireless transmission medium that carries data through the air using light beams
    Sending and receiving devices must be in line of sight
    Uses an IrDA port to enable data transfer

## Slide 20: Wireless Transmission Media
Radio transmission
  Enables music, photos, and voice to travel through the air as radio frequency or radio waves
  Bluetooth—radio transmission enables devices within 30 feet to communicate wirelessly
  Does not require direct line of sight

## Slide 21: Wireless Transmission Media

## Slide 22: Wireless Transmission Media
Microwaves
  Transmit data via electromagnetic radio waves with short frequencies

## Slide 23: Wireless Transmission Media
Satellites
  Microwave relay stations in space that transmit data through microwave signals
  Direct broadcast satellite (DBS)—consumer satellite technology that receives digital TV signals through a reception dish
  Requires the computer system to have a special communications device called a network access point—sends and receives data between computer that contain wireless adapters

## Slide 24: Wired Communication via the PSTN
Public switched telephone network (PSTN)
  Worldwide telephone system used for data and voice communications
  Primarily digital
Subscriber loop carrier (SLC)
  Links home and business telephones
  Accommodates analog devices
Local loop
  Area served by an SLC
Local exchange switch
  Digital device capable of handling thousands of calls
  Located at the local telephone’s central office

## Slide 25: Wired Communication via the PSTN

## Slide 26: Wired Communication via the PSTN
Digital telephony
  Telephones and transmissions are digital
  Companies—use a private branch exchange (PBX)
Multiplexing
  Allows multiple calls over a single line
  Long-distance carriers—transmit many calls in digital format in a single circuit

## Slide 27: Wired Communication via the PSTN
Last-mile problem
  Inability to access the PSTN’s high-speed, fiber-optic cables
  Bottleneck of data on the last mile of twisted-pair phone lines
Last-mile technologies
  Provide solutions for bottlenecks
  Used while local loops are upgraded

## Slide 28: Wired Communication via the PSTN
Last-mile technologies (con’t.)
  Integrated services digital networking (ISDN)
    Standard that provides digital telephone and data service
    No lengthy dial-in procedures or connection delay
    Requires an ISDN adapter/digital modem to connect computers to ISDN lines
    May be the only broadband solution in rural areas

## Slide 29: Wired Communication via the PSTN
Last-mile technologies (con’t.)
  Digital subscriber line (DSL) (Also called xDSL)
    Broad term for group of technologies offering high-speed access
      ADSL (asymmetric digital subscriber line)
      SDSL (symmetric digital subscriber line)
      HDSL (high bit-rate digital subscriber line)
      VDSL (very high bit-rate digital subscriber line)
    Requires DSL modem—modulate and demodulate analog and digital signals
    More expensive than dial-up—cheaper than other broadband options

## Slide 30: Wired Communication via the PSTN

## Slide 31: Wired Communication via the PSTN
Last-mile technologies (con’t.)
  Cable-based broadband
    Provides Internet access through cable TV connections
    Uses cable modems to obtain higher speeds than DSL
  Leased lines
    Specially conditioned telephone lines between two points
      Example: T1 lines

## Slide 32: Wired Communication via the PSTN
Last-mile technologies (con’t.)
  T2 and T3 lines
  SONET (synchronous optical network)
  MMDS (Multichannel multipoint distribution service)
  WiMAX (Worldwide interoperability for microwave access)

## Slide 33: Convergence: Is It a Phone or a Computer?
Digitization
  Process of transforming data into a digital form
Convergence
  Blending
  Multiple industries
    Examples: Computers, consumer electronics, telecommunications
  Products
    Examples: Personal computers, telephones

## Slide 34: Convergence: Is It A Phone or A Computer?
Cellular telephones
  Digital transmission of voice, text, images, and video
  Classified by generations—4G (fourth generation)—the current generation
  Cell sites—network of transmitters broadcasts signals throughout geographic areas called cells

## Slide 35: Convergence: Is It A Phone or A Computer?
Each cellular network includes multiple mobile switching centers (MSCs) that control communication within a set of cells.

## Slide 36: Convergence: Is It A Phone or A Computer?
  Personal communication service (PCS)
    Group of digital cellular technologies replacing most analog cellular services
    2G (second generation)—used to make smartphones, with features of phones and computing devices
    3G—more data and voice customers and higher data transfer rates
    4G—improved connectivity, data transfer rates, and support for the next generation of multimedia

## Slide 37: Convergence: Is It A Phone or A Computer?
Web-enabled devices
  Display and respond to markup languages
    Examples: HTML, XML—used to build Web pages
  Examples
    PDAs
    Smartphones—replacing PDAs
    Notebooks

## Slide 38: Convergence: Is It A Phone or A Computer?
WAP (Wireless Application Protocol)
  Standard—specifies how users can access the Web securely using:
    Pagers
    Smartphones
    PDAs
    Other wireless devices
  Requires a microbrowser

## Slide 39: Wired and Wireless Applications
Internet telephony, or VoIP (Voice over Internet Protocol)
  Offers computer-to-phone and phone-to-phone transmission through the Internet
  Placing calls requires:
    Computer with a microphone, speakers or headphones
    Internet connection
    Telephony-enabled program

## Slide 40: Wired and Wireless Applications
Internet telephony
  Videoconferencing (Web conferencing)—transmits sound and video images using:
    Video camera (Webcams)
    Skype software
  Whiteboards—enable participants to create a shared workspace
  Webcams—inexpensive, low-resolution analog or digital video cameras
  Internet TV—ability to view television shows, videos, and movies over the Internet

## Slide 41: Wired and Wireless Applications

## Slide 42: Wired and Wireless Applications
Facsimile transmission (fax)
  Transmits documents over a telephone line or the Internet using either:
    Standalone fax machine
    Computer with a fax modem and a scanner

## Slide 43: Wired and Wireless Applications
Satellite technology
  Satellite radio
    Not affected by location, distance, or obstructions
    Uses satellites orbiting the Earth
    Permits usage in areas with restricted local radio stations or poor AM/FM reception

## Slide 44: Wired and Wireless Applications
Satellite technology (con’t.)
  GPS (Global Positioning System)
    System of 27 satellites allowing a receiver to pinpoint locations
    Mobile units for cars
    Installed car systems

## Slide 45: Wired and Wireless Applications

## Slide 46: Wired and Wireless Applications

## Slide 47: Wired and Wireless Applications
Text messaging (SMS)
  Using cell phone for applications previously used on computers
  Instant messaging
  Brief e-mail

## Slide 48: Wired and Wireless Applications
Picture messaging
  MMS (multimedia messaging system)
  Transmits color pictures and backgrounds
  Cellular telephone acts as a camera
Location awareness
  Also known as position awareness
  Uses GPS-enabled chips to pinpoint the location of a cell phone
  Popular with parents of teenagers

## Slide 49: Wired and Wireless Applications
Surfing safely at public wireless hot spots
  Malicious network (evil twin)—network set up by a hacker within the operating area of a legitimate hot spot
  Use firewalls and antivirus software
  Use legitimate networks to avoid “evil twins”
  Do not perform financial transactions
  Select appropriate operating system settings to avoid being detected

## Slide 50: Wired and Wireless Applications

## Slide 51: Summary
Differentiate between bandwidth and throughput, and discuss the bandwidth needs of typical users.
Discuss how modems transform digital computer signals into analog signals and analog into digital.
List various physical and wireless transmission media and explain several transmission methods.

## Slide 52: Summary
Explain the limitations of the public switched telephone network (PSTN) for sending and receiving computer data.
Describe digital telephony and multiplexing, including their impact on line usage.
Discuss last-mile technologies that connect users with their communication providers.

## Slide 53: Summary
Provide examples of how digitization and convergence are blurring the boundaries that distinguish popular communications devices, including phones and computers.
Discuss various wired and wireless applications.

## Slide 54
All rights reserved. No part of this publication may be reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise, without the prior written permission of the publisher. Printed in the United States of America.